## Slide 1
Magnetic Circuits
Outline
Ampere’s Law Revisited
Review of Last Time: Magnetic Materials
Magnetic Circuits
Examples

## Slide 2
Electric Fields
Magnetic Fields
GAUSS
GAUSS
FARADAY
AMPERE

## Slide 3
In the case of the magnetic field we can see that ‘our old’ Ampere’s law can not be the whole story. Here is an example in which current does not gives rise to the magnetic field:
Consider the case of charging up a capacitor C which is connected to very long wires. The charging current is I. From the symmetry it is easy to see that an application of Ampere’s law will produce B fields which go in circles around the wire and whose magnitude is B(r) = μoI/(2πr). But there is no charge flow in the gap across the capacitor plates and according to Ampere’s law the B field in the plane parallel to the capacitor plates and going through the capacitor gap should be zero! This seems unphysical.
Ampere’s Law Revisited
Side
View

## Slide 4
Ampere’s Law Revisited (cont.)
If instead we drew the Amperian surface as sketched below, we would have concluded that B in non-zero !
Maxwell resolved this problem by adding a term to the Ampere’s Law.
In equivalence to Faraday’s Law, the changing electric field can generate the magnetic field:
COMPLETE
AMPERE’S LAW
Side
View

## Slide 5
Faraday’s Law and Motional emf
What is the emf over the resistor ?
There is an increase in flux through the circuit as the bar of length L moves to the right (orthogonal to magnetic field H) at velocity, v.
In a short time Δt the bar moves a distance Δx = v*Δt, and the flux increases by ΔФmag = B (L v*Δt)
from Chabay and Sherwood, Ch 22

## Slide 6
Faraday’s Law for a Coil
The induced emf in a coil of N turns is equal to N times the rate of change of the magnetic flux on one loop of the coil.
Will the current run CLOCKWISE or ANTICLOCKWISE ?
from Chabay and Sherwood, Ch 22
Moving a magnet towards a coil produces a time-varying magnetic field inside the coil
Rotating a bar of magnet (or the coil) produces a time-varying magnetic field inside the coil

## Slide 7
Complex Magnetic Systems
Magnetic Circuits: Reduce Maxwell to (scalar) circuit problem
Energy Method: Look at change in stored energy to calculate force
DC Brushless
Stepper Motor
Reluctance Motor
Induction Motor
We need better (more powerful) tools…

## Slide 8
Magnetic Flux Φ [Wb] (Webers)
Magnetic Flux Density B [Wb/m2] = T (Teslas)
Magnetic Field Intensity H [Amp-turn/m]
due to macroscopic & microscopic
due to macroscopic currents
Faraday’s Law
and

## Slide 9
Example: Magnetic Write Head
Bit density is limited by how well the field can be localized in write head
Horizontal
Magnetized Bits
Shield
Ring Inductive
Write Head
Recording Medium
GMR
Read
Head

## Slide 10
Review: Ferromagnetic Materials
hysteresis
0
B
H
H : coercive magnetic field strength
B : remanence flux density
B : saturation flux density
C
r
S
B,J
H
0
Slope =
i
Behavior of an initially unmagnetized
material.
Domain configuration during several stages
of magnetization.
Initial
Magnetization
Curve

## Slide 11
Thin Film Write Head
How do we apply Ampere’s Law to this geometry (low symmetry) ?
Recording Current
Magnetic Head Coil
Magnetic Head Core
Recorded Data
Recording Magnetic
Field

## Slide 12
Electrical Circuit Analogy
Charge is conserved…
Flux is ‘conserved’…
Electrical
Ф
Magnetic
EQUIVALENT
CIRCUITS
+

## Slide 13
Electrical Circuit Analogy
Electromotive force (charge push)=
Magneto-motive force (flux push)=
Electrical
Ф
Magnetic
EQUIVALENT
CIRCUITS
+

## Slide 14
Electrical Circuit Analogy
Material properties and geometry determine flow – push relationship
Recovering macroscopic variables:
OHM’s LAW

## Slide 15
Reluctance of Magnetic Bar
Magnetic “OHM’s LAW”

## Slide 16: Flux Density in a Toroidal Core
i
(of an N-turn coil)
N turn
coil
Core centerline

## Slide 17
Electrical Circuit Analogy
Electrical | Magnetic
Voltage | Magnetomotive Force
Current | Magnetic Flux
Resistance | Reluctance
Conductivity | Permeability
Current Density | Magnetic Flux Density
Electric Field | Magnetic Field Intensity

## Slide 18
Toroid with Air Gap
Why is the flux confined mainly to the core ?
Can the reluctance ever be infinite (magnetic insulator) ?
Why does the flux not leak out further in the gap ?
A = cross-section area
Electric
current
Magnetic
flux

## Slide 19
Fields from a Toroid
A = cross-section area
Electric
current
Magnetic
flux

## Slide 20
Scaling Magnetic Flux
&
Same answer as Ampere’s Law (slide 9)
A = cross-section area
Electric
current
Magnetic
flux

## Slide 21
Magnetic Circuit for ‘Write Head’
A = cross-section area
i
N=500
2cm
8cm
2cm
0.5cm
+ -
Core Thickness = 3cm

## Slide 22
Parallel Magnetic Circuits
A = cross-section area
10cm
10cm
0.5cm
1cm
i
Gap a
Gap b

## Slide 23: A Magnetic Circuit with Reluctances in Series and Parallel
“Shell Type” Transformer
+
-
+
-
v1
v2
N1 turns
λ1
N2 turns
λ2
Depth A
l2
l1
l=l1+l2
Magnetic Circuit
+
+
-
-

## Slide 24
Faraday Law and Magnetic Circuits
Flux linkage
Step 2: Estimate voltage v2 due to time-varying flux…
Step 1: Estimate voltage v1 due to time-varying flux…
sinusoidal
A = cross-section area
+
v1
-
+
v2
-
Ф
N1
N2
+
-
i1
i2
Load
Primary
Secondary
Laminated Iron Core

## Slide 25
Complex Magnetic Systems
Magnetic Circuits: Reduce Maxwell to (scalar) circuit problem
Energy Method: Look at change in stored energy to calculate force
DC Brushless
Stepper Motor
Reluctance Motor
Induction Motor
Powerful tools…
Makes it easy to calculate B, H, λ

## Slide 26
Stored Energy in Inductors
In the absence of mechanical displacement…
For a linear inductor:
Stored energy…

## Slide 27
Relating Stored Energy to Force
Lets use chain rule …
This looks familiar …
Comparing similar terms suggests …

## Slide 28
Energy Balance
heat
electrical
mechanical
For magnetostatic system, dλ=0 no electrical power flow…
neglect heat

## Slide 29
Linear Machines: Solenoid Actuator
Coil attached to cone
If we can find the stored energy, we can immediately compute the force…
…lets take all the things we know to put this together…

## Slide 30
KEY TAKEAWAYS
COMPLETE AMPERE’S LAW
RELUCTANCE
Electrical | Magnetic
Voltage | Magnetomotive Force
Current | Magnetic Flux
Resistance | Reluctance
Conductivity | Permeability
Current Density | Magnetic Flux Density
Electric Field | Magnetic Field Intensity

## Slide 31
MIT OpenCourseWare
http://ocw.mit.edu
6.007 Electromagnetic Energy: From Motors to Lasers
Spring 2011
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.