## Slide 1
Motors and Engines
Outline
Review of Last Time
Equivalent Circuit for Motor
Homopolar Rotor
Notes: DEMOS:
Go cart power consumed as it starts/runs
Homopolar motor
Lab motor

## Slide 2
BATTERY
ELECTRICAL MOTOR
FORWARD
NEUTRAL
REVERSE
To begin to understand the value of liquid fuels
(and the origins of the energy crisis facing the world)
we will make measurements and calculations on our go-cart.
Electrical to Mechanical Energy Conversion
Go-cart designed and built by Prof. Steven B. Leeb,

## Slide 3
The first law of thermodynamics
“Energy is conserved”
Energy Flows in the Go-Cart
System of interest, e.g., Some type of Go-cart

## Slide 4
The ports of many energy conversion systems are conveniently described by a set of “through” and “across” measurements or variables. The different types of “through” and “across variables” distinguish different types of engineers (electrical, mechanical, chemical, etc.). The first and second laws apply to everyone.
“ACROSS” variables typically measure how hard we are “pushing”. Typical “across” variables include:
Force, from mechanical engineering, measured in Newtons (N = kg*m/(s*s))
Voltage, from electrical engineering, measured in volts (V)
Torque, or twisting force, from mechanical engineering, measured in N-m
Pressure, from ocean/aero engineering, measured in N/(m*m)
Associated “THROUGH” variables typically measure how much “stuff” is flowing:
Velocity, from mechanical engineering, measured in meters/sec (m/s)
Current, from electrical engineering, measured in Coulombs/sec or Amps
Angular Velocity, from mechanical engineering, measured in rads/sec
Flow, from ocean/aero engineering, measured in volume/sec or m*m*m/s
Review - Across and Through Variables
POWER is the product of an “across” variable and a “through” variable.

## Slide 5
Let’s Drive the Electric Go-Cart on a Level Smooth Surface
Measure the voltage across the drive motor terminals and the current flowing
into the motor when the go-cart reaches a “steady-state” or cruising speed.
In steady state, our measurements are:
Current flowing into the motor = 15 A
Voltage across the motor terminals = 36 V
Steady-state velocity of the cart = 12 miles/hour
Now, calculate the steady-state power consumed by the electric motor = 540 W
Range of the go-cart
at the steady state-velocity = 13.6 miles
Some statistics about the go-cart and it’s components:
Battery pack = 36 volts (nominal), 17 Amp-hours capacity
(can provide 17 amps for 1 hour, or 1 amp for 17 hours)
Battery pack weighs 36 pounds

## Slide 6
Why does the Go-Cart use Energy when Moving at a Steady-State Velocity ?
When the cart is moving, it has a certain amount of stored or “kinetic” energy. In steady-state, the velocity of the vehicle is constant, and the stored kinetic energy of the vehicle is also constant. Nevertheless, the electric motor in the go-cart consumes a certain amount of power or energy per second while the go-cart was driving at a steady speed.
Where does this energy go?
What physical mechanisms in the cart consume energy while the cart is moving?
Microscopic Heat & Friction

## Slide 7
Rotational Dyanamics (Quick Review)
Linear | Rotational
x | θ
F | τ
F = m a | τ = Ι α
Friction force = b v | Friction torque = β ω
Work = F d | Work = τ θ
Power = F v | Power = τ ω

## Slide 8
The go-cart motor is NOT a resistor !!! It does not obey Ohm’s Law.
VOLT METER
SWITCH
Forward-Off-Reverse
CLAMP-ON AMMETER
High-Level Model of Motor
NEGLECT MOTOR INDUCTANCE
(STORED MAGNETIC ENERGY)
RESISTANCE OF MOTOR WINDINGS
WHEN MOTOR TURNS IT GENERATES “Back EMF”
Go-cart designed and built by Prof. Steven B. Leeb,

## Slide 9
MOTOR: When we put electrical energy into the lossless motor,
it must “come out” as motion of the mechanical shaft.
GENERATOR: If we put mechanical energy into the shaft (by turning it)
it must “come out” the electrical port.
The 1st Law requires that any contraption that can be used as an electromechanical actuator, i.e., some kind of motor, can also be used, somehow, as a generator.
The dependent source or “Back EMF” is a convenient circuit symbol to acknowledge our understanding of this first law requirement. If we put electrical power into the source, it “transduces” it to mechanical shaft power. If we turn the shaft, we must generate a voltage.
A Loudspeaker is Another Device Example of the 1st Law:
If we drive a speaker electrically, it makes sound (a typical loudspeaker or motor). If we talk into the speaker, it makes a voltage (a typical microphone or generator).
Back Electromotive Force

## Slide 10
The go-cart motor is NOT a resistor !!! It does not obey Ohm’s Law.
High-Level Model of Motor
is the torque from the motor
In steady-state, turning at a constant velocity … the net torque is zero
How do we relate the current/voltage to the torque ?
Energy balance (from yesterday) tells us that …

## Slide 11
A Closer Look at Motors
Go-cart designed and built by Prof. Steven B. Leeb,

## Slide 12
Homopolar Generator
Note that this law does not explain forces on dielectrics or magnetically permeable materials. Most common actuators employ these forces.
Torque is proportional to Current
KNOWN AS THE “MOTOR CONSTANT”

## Slide 13
Torque is
proportional to current
IF WE APPLY STEADY CURRENT ON THE MOTOR
… then in steady state operation …
STEADY STATE
CONSTANT WHICH DEPENDS
on FRICTION COEFFICIENT and MOMENT ARM
(EMPIRICALLY DETERMINED)
ANGULAR VELOCITY
Motor Torque and Angular Velocity (when STEADY CURRENT is applied)

## Slide 14
The go-cart motor is NOT a resistor !!! It does not obey Ohm’s Law.
HIGH-LEVEL MODEL of a MOTOR
IF WE APPLY STEADY VOLTAGE, Va , ON THE MOTOR
… then in steady state operation …
Current through the motor in the steady state is
Motor Torque and Angular Velocity (when STEADY VOLTAGE is applied)

## Slide 15
When we plot the steady state ωss as a function of K we find that for a given voltage, the motor reaches the maximum speed when

## Slide 16
There are lots of different motors…
DC Brushless
Stepper Motor
Reluctance Motor
Induction Motor
The E&M can be intimidating as you have to keep track of …
… time-varying fields
… wild geometries
… magnetic materials and coils
… rotational dynamics
http://www.freescale.com/files/microcontrollers/doc/train_ref_material/MOTORTUT.html
Electrical motors can convert electrical energy into motion with 90% efficiency
© Freescale Semiconductor, Inc. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/fairuse.

## Slide 17
Let’s Drive the Electric Go-Cart on a Level Smooth Surface
Measure the voltage across the drive motor terminals and the current flowing
into the motor when the go-cart reaches a “steady-state” or cruising speed.
In steady state, our measurements are:
Current flowing into the motor = 15 A
Voltage across the motor terminals = 36 V
Steady-state velocity of the cart = 12 miles/hour
Now, calculate the steady-state power consumed by the electric motor = 540 W
Range of the go-cart
at the steady state-velocity = 13.6 miles
Some statistics about the go-cart and it’s components:
Battery pack = 36 volts (nominal), 17 Amp-hours capacity
(can provide 17 amps for 1 hour, or 1 amp for 17 hours)
Battery pack weighs 36 pounds

## Slide 18
Energy Losses of the Electrical Go-Cart
We have estimated the electrical losses (resistance) by carefully measuring the terminal resistance of the motor with a good ohm meter at several rotor positions and then averaged the results to compute approximately 1.2 ohms. There may be other electrical losses not accounted by this method, but this is a start.
Using our current, voltage, and speed measurements:
What is the electrical power loss for the
go-cart in steady-state driving? 270 W
What, therefore, must be the power lost
to mechanical friction in steady state? 270 W
Notes: Power loss = i^2 * R = 15^2 * 1.2 = 270

## Slide 19
Hypothetical Gas-Powered Go-Cart:
Let’s make a comparison to a similar go-cart powered by a reasonably sized gasoline engine and gas tank. Let’s replace the 36 pounds of batteries by a gas tank that holds 36 pounds of gasoline.
- Gasoline weighs 6 pounds per gallon,
- Gasoline stores 40,000 Watt-hours of heat energy per gallon. That is, if you burned a gallon of gasoline, you would get 40,000 Watt-hours worth of heat.
How many joules are stored in a gallon
of gasoline? 144,000,000 J
How many gallons of gas are stored in the
hypothetical go-cart gas tank? 6 gallons
How many joules of heat energy are stored in
the go-cart gas tank? 864 MJ
- With 10% efficient engine we can deliver 86.4 MJ of mechanical energy
- We need 270 W to operate the car … so we can operate it for …
… 320,000 seconds = 88.8 hours ~ 1,000 miles (at the speed of 12 miles/hour)

## Slide 20
Which go-cart is more energy efficient?
Which go-cart is more economical ?
ELECTRICAL
GAS-POWERED
vs.
17 A-hour battery at 36 V
(or 614 W-hours)
To charge the battery we need to burn coal (in a power plant) at 30% efficiency and run an efficient mechanical motor with up to 90% efficiency  27% efficient process of converting coal energy into motion
Average national cost of electrical energy is ~$0.10 per kW-hour To charge the battery we then spent
0.614 kW-hr * $ 0.10 (kW-hr)-1 = $0.06
 $.005 per mile
Gas powered car engines are
~10% efficient
For the 6 gallons of gasoline we spent
6 * $3 = $18
and we traveled 1,000 miles
 $.018 per mile

## Slide 21
CAPACITOR
BATTERY
GASOLINE
1 gallon:
13 kW-hr/kg
Prius NiMH:
0.035 kW-hr/kg
Next Time we will consider
different methods of
Energy Storage in Hybrid Vehicles
to solve the “mystery” of why gasoline is so efficient in storing energy
In each case, energy is stored in charge separation …
Prius in Public Domain
Image is in Public Domain

## Slide 22
Energy stored in 1 gallons of gasoline is 35 kW-hr (or rounding-up 40 kW-hr)
This is equivalent to the energy stored in each of the following:
20 fast-food meals (burger, fries, drink, at 1,500 calories per meal). The human body converts the chemical energy from food into mechanical energy and body heat. When you buy food, you are buying energy to keep your body running.
1 piece of firewood (15 pounds piece, 20% moisture). Firewood is the major source of energy in many parts of the world.
10 pounds of coal. Coal is the most abundant fossil fuel on earth. It is a major source of fuel for power plants.
1.198 therms of natural gas. Natural gas is sold by the therm. A therm is equivalent to 100,000 British Thermal Units (BTU) of energy, and it takes about a hundred cubic feet of natural gas to make up a therm.
2145 pounds of lead-acid batteries. The energy stored in lead acid batteries starts cars and runs golf carts and electric cars.
1 gallon of gasoline weighs 6 lbs ~ 2.75 kg
The bulk of a typical gasoline consists of hydrocarbons with between 5 and 12 carbon atoms per molecule.

## Slide 23
When motor turns it generates “Back EMF”
The 1st Law requires that any contraption that can be used as an electromechanical actuator can use its actuation to generate EM fields: - a motor can also be used as a generator. - a loudspeaker can also be used as a microphone
Torque of a motor = motor constant × motor current
When frictional torque in a motor equals the morque from the Lorentz force inside the motor, the net torque is zero and a steady operation is achieved.
Frictional Torque = constant × angular velocity
Operated at CONSTANT CURRENT – motors have steady angular velocity
Opertated at CONSTANT VOLTAGE – motors have steady torque
Energy stored in 1 gallons of gasoline is 35 kW-hr (or rounding-up 40 kW-hr)
Electric vehicles are more economical per mile traveled, however, they can travel fewer miles since the batteries store less energy per kg than fuel does
KEY TAKEAWAYS

## Slide 24
MIT OpenCourseWare
http://ocw.mit.edu
6.007 Electromagnetic Energy: From Motors to Lasers
Spring 2011
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.