## Slide 1
Faraday’s Law (Induced emf)
Outline
Magnetic Flux and Flux Linkage
Inductance
Stored Energy in the Magnetic Fields of an Inductor
Faraday’s Law and Induced Electromotive Force (emf)
Examples of Faraday’s Law
Reading - Shen and Kong – Ch. 16

## Slide 2
Magnetic Flux Φ [Wb] (Webers)
Magnetic Flux Density B [Wb/m2] = T (Teslas)
Magnetic Field Intensity H [Amp-turn/m]
due to macroscopic & microscopic
due to macroscopic currents

## Slide 3
Flux Linkage of a Solenoids
FOR A SUFFICIENTLY LONG SOLENOID…
S
B
In the solenoid the individual flux lines pass through the integrating surface S more than once
B = Magnetic flux density inside solenoid
A = Solenoid cross sectional area
N = Number of turns around solenoid
… flux linked by solenoid

## Slide 4
Inductors
… is a passive electrical component that stores energy in a magnetic field created by the electric current passing through it. (This is in equivalence to the energy stored in the electric field of capacitors.)
An inductor's ability to store magnetic energy is measured by its inductance, in units of henries. The henry (symbol: H) is named after Joseph Henry (1797–1878), the American scientist who discovered electromagnetic induction independently of and at about the same time as Michael Faraday (1791–1867) in England.
The magnetic permeability of the vacuum: [henry per meter]
EQUIVALENCE OF UNITS:
FOR A LINEAR COIL:
IN GENERAL:

## Slide 5
Stored Energy in an Inductor
If L is not a function of time …
… where E is energy stored in the field of the inductor any instant in time
FROM 8.02:
 voltage over an inductor
FOR A LINEAR COIL:

## Slide 6
Calculation of energy stored in the inductor

## Slide 7
General: Stored Energy in the Coil
… where Ws is energy stored in the field of the inductor any instant in time
FROM 8.02:
 voltage over an inductor
Since then
 Change in the magnetic flux within the inductor generates voltage

## Slide 8
Michael Faraday in 1831 noticed that time-varying magnetic field produces an emf in a solenoid
from Chabay and Sherwood, Ch 22
Induced electromotive force (emf)

## Slide 9
THEREFORE, THERE ARE TWO WAYS TO PRODUCE ELECTRIC FIELD
(1) Coulomb electric field is produced by electric charges according to Coulomb’s law:
(2) Non-Coulomb electric field ENC is associated with time-varying magnetic flux density dB/dt
For a solenoid, ENC
- curls around a solenoid
- is proportional to -dB/dt through the solenoid
- decreases with 1/r, where r is the radial distance from the solenoid axis
=0

## Slide 10
What is the Direction of Magnetically Induced (non-Coulomb) Field, ENC ?
Find the change in the magnetic flux density as a basis for determining the direction of
Lenz’s Rule
The induced electric field would drive the current in the direction to make the magnetic field that attempts to keep the flux constant
B out, increasing
B out, decreasing
B in, increasing
B in, decreasing
into page
into page
out of page
out of page

## Slide 11
Magnetically Induced (non-Coulomb) ENC
Drives Current in a Loop Surrounding the Solenoid
METAL RING IS PLACED AROUND A SOLENOID
END VIEW: The non-Coulomb electric field drives a current I2 in the ring
This pattern of surface charge is impossible, because it would imply a huge E at the marked location, and in the wrong direction !

## Slide 12
Integral of ENC along a path that does not encircle the solenoid is zero since ENC ~ 1/r
where R is the ring resistance
What if we double the value of r2 ?  Still get the same emf around the loop
emf in a ring encircling the solenoid is the same for any radius
B inside solenoid increasing with time

## Slide 13
Will Current Run in these Wires ?
Wire

## Slide 14
Example
from Chabay and Sherwood, Ch 22
An ammeter measures current in a loop surrounding the solenoid. Initially I1 is constant, so B1 is constant, and no current runs through the ammeter.
Vary the solenoid current I1 and observe the current I2 that runs in the outer wire, through the ammeter

## Slide 15
Peculiar Circuit – Two Bulbs Near a Solenoid
Loop 1: emf - R1I1 – R2I2 = 0
Loop 2: emf - R1I1 = 0
Loop 3: R2I2 = 0 (no flux enclosed)
Two light bulbs connected around a long solenoid with varying B.
… Add a thick copper wire.

## Slide 16
Question:
If we use a solenoid with twice the cross-sectional area, but the same magnetic flux density (same magnitude of I1), what is the magnitude of I2 ?
We can build the solenoid with the larger cross-sectional area, 2*A, out of two solenoids with the initial cross-sectional area, A. Each of the smaller solenoids would induce current I2, so by superposition, for the twice-as-big solenoid the current would be twice-as-big !

## Slide 17
Faraday’s Law
The induced emf along a round-trIp path is equal to the rate of change of the magnetic flux on the area encircled by the path.

## Slide 18
Faraday’s Law and Motional emf
What is the emf over the resistor ?
There is an increase in flux through the circuit as the bar of length L moves to the right (orthogonal to magnetic field H) at velocity, v.
In a short time Δt the bar moves a distance Δx = v*Δt, and the flux increases by ΔФmag = B (L v*Δt)

## Slide 19
Terminal Voltages & Inductance
Assume:
Perfectly conducting wire
Stationary contour C
Negligible magnetic flux at the terminals
If the current i created the magnetic flux density B, then the flux linkage is given by λ = Li. In this case, emf = L di/dt. L is the self inductance of the coil.
emf = dλ/dt

## Slide 20
Faraday’s Law for a Coil
The induced emf in a coil of N turns is equal to N times the rate of change of the magnetic flux on one loop of the coil.
Will the current run CLOCKWISE or ANTICLOCKWISE ?
Moving a magnet towards a coil produces a time-varying magnetic field inside the coil
Rotating a bar of magnet (or the coil) produces a time-varying magnetic field inside the coil

## Slide 21
A long solenoid passes through a loop of wire…

## Slide 22
Electric Fields
Magnetic Fields
GAUSS
GAUSS
FARADAY
AMPERE

## Slide 23
Next …
MAGNETIC MATERIALS
MAGNETIC CIRCUITS
Image is in the public domain

## Slide 24
KEY TAKEAWAYS
FOR A SUFFICIENTLY LONG SOLENOID…
INDUCTANCE:
UNITS of INDUCTANCE:
ENERGY STORED in an INDUCTOR:
THERE ARE TWO WAYS TO PRODUCE ELECTRIC FIELD
Coulomb electric field is produced by electric charges according to Coulomb’s law
Non-Coulomb electric field ENC is due to time-varying magnetic flux density dB/dt
Faraday’s Law: The induced emf along a round-trIp path is equal to the rate of change of the magnetic flux on the area encircled by the path.
Lenz’s Rule:
The induced electric field would drive the current in the direction to make the magnetic field that attempts to keep the flux constant

## Slide 25
MIT OpenCourseWare
http://ocw.mit.edu
6.007 Electromagnetic Energy: From Motors to Lasers
Spring 2011
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.